## Slide 1
10CSC7 19 Haratua 2015
What we will do | What we will learn
Preliminaries and roll | The importance of starting well
Learn how to compare and contrast circuits | How to move past the basics to the tougher qu’s
If time, work on Scipad pages 66 – 70 | How to do test-type questions
Revisit the objectives of the unit | Whether we have covered the objectives or not.
Set a date for the test(s) and begin Mr H’s HDSDRM | How to make best use of the learning available

## Slide 2
HW item | Skills practiced
Scipad pages 125 - 143 Due already | DNA and genetics
Scipad pages 10, 11, 12, 14 Due Zenday 37th of Octember | Atoms and atomic structure
Topic Test: Atomic Structure Wed 22 April 2015 | Atoms and atomic structure

## Slide 4
Compare an contrast the two circuits. You should include:
A description of the type of circuits and the brightnesses of each lamp
An explanation of the path of electrons around the circuit and the part played by the power supply in the circuit
Links between the power calculations you made earlier and the brightnesses of the lamps
A discussion of the power outputs for each of the two circuits.

## Slide 5
Circuit 1 is a series circuit. Lamps are dim and this is because:
Electrons have only one possible path
Each electron gets 7.5 Volts and has to share/split this between two lamps
Each lamp receives about half of the energy (if it is symmetrical)
Circuit 2 is a parallel circuit. Lamps are bright and this is because:
Electrons have a choice of two possible paths
Each electron gets 7.5 Volts and does not have to share this between two lamps; all that energy is given to the lamp the electron went through
Each lamp receives all the energy given by the electricity source (and the current put out by the source doubles because there are two users of current – in parallel

## Slide 6
In circuit 1, both lamps together use P=VI, P=7.5x0.15, P=1.125W.
If we assume that the lamps are the same then each lamp gets about 0.56 Watts.
If we take it that the lamps in circuit 2 are the same type then each one is using P=VI, P= 7.5x0.25, P= 1.875 Watts each.
The second circuit uses more energy/power than the first one because the current is greater. Each branch uses more current without having to share/split the available voltage – which is what happens in circuit 1 because it is a series circuit.