## Slide 1
Notes: Created by Educational Technology Network. www.edtechnetwork.com 2009
<number>

## Slide 2
Electrical Definitions | Circuit Drawing | Parallel Circuits | Series Circuits | Miscellany
10 | 10 | 10 | 10 | 10
20 | 20 | 20 | 20 | 20
30 | 30 | 30 | 30 | 30
40 | 40 | 40 | 40 | 40
50 | 50 | 50 | 50 | 50
60 | 60 | 60 | 60 | 60
70 | 70 | 70 | 70 | 70
80 | 80 | 80 | 80 | 80
90 | 90 | 90 | 90 | 90
Notes: <number>

## Slide 3: Question 1 - 10
What is the symbol for an Ammeter, and how do you use it in a circuit?
A
Ammeters are always wired in series (in the same loop) as the component that
Notes: <number>

## Slide 4: Question 1 - 20
What is current and what is the unit of current?
Current is the flow of electrons in a circuit. It is measured in Units called Amperes (Amps)
Notes: <number>

## Slide 5: Question 1 - 30
What is Voltage and what is the unit of voltage?
Voltage is the amounf of Energy in a Circuit. It is measure in Volts (V)
Notes: <number>

## Slide 6: Question 1 - 40
How is the power in a circuit calculated?
Power is calculated by Voltage x Current
P=V I
Notes: <number>

## Slide 7: Question 1 - 50
What is the Resistance and how is it calculated?
Resistance is the opposition to the current in a circuit. It is calculated by R=V/I or Voltage / Current
Notes: <number>

## Slide 8: Question 1 - 60
What is the power in the bulb?
10V
1.5A
Power is Voltage x Current
P = VI
= 10V x 1.5A
=15W
Notes: <number>

## Slide 9: Question 1 - 70
What is the symbol for a Voltmeter and how is it wired into a circuit?
V
Voltmeters are wired in parallel to the component being measured.
Notes: <number>

## Slide 10: Question 1 - 80
Calculate the power in the bulb 1
10V
1.5A
Bulb 1
Power = Voltage x Current
The bulbs are in series. The Current will be the same everywhere in the circuit. Therefore the I=1.5A
The voltage in the circuit is divided between the components in series. Therefore V = 10V/2 (for the 2 bulbs) = 5V
P=VI
P=5Vx1.5A
P=7.5W
Notes: <number>

## Slide 11: Question 1 - 90
Calculate the power in bulb 1
10V
1.5A
Bulb 1
Power = Voltage x Current
The bulbs are in parallel. The Current will divided among the branches. We assume the bulbs are the same size.Therefore the I=1.45A/2 = 0.75A
The voltage in a parallel circuit does not diminish when it branches. Therefore V = 10V
P=VI
P=10Vx0.75A
P=7.5W
Notes: <number>

## Slide 12: Question 2 - 10
What is this the symbol for and what does this component do?
This is a resistor. It turns electrical energy into heat energy
Notes: <number>

## Slide 13: Question 2 - 20
Explain the differences between these two symbols and what that means for a circuit
The top symbol is an open switch. The bottom symbol is a closed switch. For an electrical circuit to function the switch needs to be closed in order to complete the circuit and allow an unbroken path for the electrons to travel
Notes: <number>

## Slide 14: Question 2 - 30
What are the rules of circuit drawing?
Use a ruler
All lines must be square
No overlapping lines or gaps in lines
Notes: <number>

## Slide 15: Question 2 - 40
What two things are wrong with this circuit drawing?
The lines do not meet properly, and one of the cells is backward.
Notes: <number>

## Slide 16: Question 2 - 50
What is wrong with this circuit?
It is not drawn with a ruler and lines overlap
Notes: <number>

## Slide 17: Question 2 - 60
What is wrong with this circuit?
A
A
Ammeters are wired in series not parallel.
Notes: <number>

## Slide 18: Question 2 - 70
What is wrong with this circuit?
V
V
Voltmeters are wired in parallel not series
Notes: <number>

## Slide 19: Question 2 - 80
Describe this circuit
This circuit is powered by two cells. It has three lamps, on two parallel circuits. One branch has one lamp and the second branch has two lamps.
Notes: <number>

## Slide 20: Question 2 - 90
Redraw this circuit correctly
V
The lines are all ruled and square. The power supply is at the top.
There are no gaps in the circuit wires, nor any overhanging wires.
No component is on a corner
Notes: <number>

## Slide 21: Question 3 - 10
Describe a parallel circuit.
A Parallel circuit occurs when there is more than one path for the electrical current to take. If one of the paths breaks, the other paths are not affected.
Notes: <number>

## Slide 22: Question 3 - 20
What does voltage do in a parallel circuit?
In a parallel circuit the voltage of each branch of the circuit is the same.
Notes: <number>

## Slide 23: Question 3 - 30
What does Current do in a Parallel circuit?
In a Parallel circuit the current produced by the power source is divided among the branches according to the load on each branch.
The sum of the current in the branches is the same as the current in the main part of the circuit.
Notes: <number>

## Slide 24: Question 3 - 40
What is the voltage in Bulb 1 and Bulb 2?
Bulb 1
Bulb 2
The voltage is each bulb is the same and is the same as the voltage produced by the power supply. In this case the voltage in each bulb is 6V
6V
Notes: <number>

## Slide 25: Question 3 - 50
What is the current in Bulb 1 and Bulb 2?
Bulb 1
Bulb 2
The current in the main circuit is divided between the branches. In this case because the load on each branch is the same the current is divided equally and each bulb has 1.5A of current
3A
Notes: <number>

## Slide 26: Question 3 - 60
What is the Voltage of V1 and V2?
V2=
V=12V
V1=
The current is the same in each branch of a parallel circuit. Therefore the Voltage of both V1 and V2 are each 12V
Notes: <number>

## Slide 27: Question 3 - 70
What is the Current at I1 and I2?
I= 3A
I2=
I1
The current is distributed to the branches of the parallel circuit. Assuming the bulbs are the same I2= 3A and therefore A1=6A
Notes: <number>

## Slide 28: Question 3 - 80
What is the Current at I1 and I2?
15A
I2
A1
The current in a parallel circuit isdistributed between the branches. Assuming that the two bulbs are the same the current would be evenly distributed. Therefore at I2 the current would be 15A and at I1 the current would be 30A
Notes: <number>

## Slide 29: Question 3 - 90
Calculate the Power required in bulb 1
Bulb 1
Bulb 2
20V
15A
P = VI
Current in Bulb 1 is 15V/2 = 7.5V
Voltage in Bulb 1 is 20V
PBulb 1 =V Bulb 1 x I Bulb 1
= 7.5A x 20V
= 150W
Notes: <number>

## Slide 30: Question 4 - 10
Describe a series circuit.
A series circuit is where the components are linked in one continuous loop. If one part of the circuit breaks all components stop working
Notes: <number>

## Slide 31: Question 4 - 20
What does voltage do in a series circuit?
In a series circuit the voltage provided by the power source is divided among the components in the circuit..
Notes: <number>

## Slide 32: Question 4 - 30
What does Current do in a series circuit?
In a series circuit the current is the same throughout the circuit.
Notes: <number>

## Slide 33: Question 4 - 40
What is the voltage in Bulb 1 and Bulb 2?
Bulb 1 Bulb 2
The voltage provided by the power source is divided between the components in the circuit. In this case each bulb has a voltage of 3V
6V
Notes: <number>

## Slide 34: Question 4 - 50
What is the current in Bulb 1 and Bulb 2?
The current is the same at every point in a series circuit. In this case Bulb 1 and Bulb 2 each have I=24A
Bulb 1 Bulb 2
24A
Notes: <number>

## Slide 35: Question 4 - 60
What is the Voltage of V1 and V2?
The Voltage is shared equally among the components in a series circuit. Therefore assuming that the two bulbs are the same V1=12V.
V2 is therefore 24V
V1 V=12V
V2
Notes: <number>

## Slide 36: Question 4 - 70
What is the Current at I1 and I2?
I1 I = 12A
I2
The current is the same at all points in a series circuit, therefore I1=12A and I2= 12A
Notes: <number>

## Slide 37: Question 4 - 80
What is the Voltage provided by the power source?
The voltage in a series circuit is divided between the components in the circuit. In this case the bulbs are different so the Voltage is distributed unevenly. The Voltage of the power source is the sum of the voltage being used by the components. In this case it is 18V
12V 6V
Notes: <number>

## Slide 38: Question 4 - 90
Calculate the Power required in bulb 1
P = VI
Current in Bulb 1 is 20A
Voltage in Bulb 1 is 12V/2 = 6V
PBulb 1 =V Bulb 1 x I Bulb 1
= 20A x 6V
= 120W
Bulb 1
12V
20A
Notes: <number>

## Slide 39: Question 5 - 10
Explain the difference between the two pictures.
4.5A
6V
4.5A
6V
The symbol on the left is for three cells in a battery. The symbol on the right is for a power pack run on mains electricity
Notes: <number>

## Slide 40: Question 5 - 20
What is the Voltage and current in each bulb?
12V
6A
Each branch of the parallel circuit will have the same voltage as produced by the power source. As there are two bulbs in series on each branch the voltage on each branch will be shared. Therefore the bulbs will each have 6V.
The current branches in a parallel circuit but is the same at all points in a series circuit. Therefore the Current in each branch and each bulb is 3A
Notes: <number>

## Slide 41: Question 5 - 30
Explain why Bulb A is brighter than Bulbs B and C
12V
6A
Bulb A
Bulb B
Bulb C
Bulb brightness is controlled by the amount of Power running through the bulb.
Bulb A has 12V of energy powering it.
Bulbs B and C shared the 12V of energy and have 6V each
All the bulbs have 6A of Current
Therefore Bulb A has 72W powering it, but Bulbs B and C each have 36W so don’t glow as brightly
Notes: <number>

## Slide 42: Question 5 - 40
Draw the circuit with a voltmeter and an ammeter to measure Bulb A
A
V
Notes: <number>

## Slide 43: Question 5 - 50
Explain what Electricity is
Electricity is energy carried by the movement of electrons. It can be moving (current) or static (a build up of electrons).
Notes: <number>

## Slide 44: Question 5 - 60
How much Power is used to supply at bulb running on 240V and 0.25A?
P = V x I
= 240V x 0.25A
= 60W
Notes: <number>

## Slide 45: Question 5 - 70
What is the role of the power supply in a circuit?
The power supply refers to cells, batteries, or power pack in a circuit. It provides the electrons that travel in a circuit and determines the amount of current and voltage that a circuit has.
Notes: <number>

## Slide 46: Question 5 - 80
Calculate the Power of the bulb in the following circuit
0.28A
6.54V
P = V I
= 6.54V x 2.8A
= 18.3W
Notes: <number>

## Slide 47: Question 5 - 90
What is the current in a 100W bulb running at 12.5V
P=V I
I=P/V
= 100W/12.5V
= 8A
Notes: <number>