## Slide 1: CAPACITORS

## Slide 2
A capacitor is a device used to “store” electric charge.
It can store energy and release it very quickly!!

## Slide 3: Some hybrid buses uses capacitors instead of batteries

## Slide 4: So do some other new vehicles

## Slide 5: Kinetic torches store energy in a capacitor

## Slide 6: Speakers use capacitors to direct current to the correct speaker

## Slide 7: What determines the amount of air you can squeeze in a bottle?
More pressure
More volume

## Slide 8: What affects the amount of charge in a capacitor?
More voltage
More capacitance

## Slide 9
A resistor is an object.
Its resistance is how much it opposes the flow of charge. (measured in Ω)
A capacitor is an object.
Its capacitance is how much charge it can store. (measured in Farads (F))

## Slide 10
Charge stored = Capacitance x Voltage
Q = C x V
A 1 Farad capacitor will store one Coulomb of charge if connected to a one Volt cell.

## Slide 11
Capacitor Animation

## Slide 12: Pumping Air Into a Bottle
pressure
time
time
Air flow

## Slide 13: Charging a Capacitor
What happens when the switch is closed?

## Slide 14: Charging a Capacitor
voltage
time
time
current
batteryvoltage

## Slide 15
electron flow
electron flow

## Slide 16
link to phet AC

## Slide 17
time
Battery voltage
voltage
0.63 Vmax
1 time constant
0.37 Vmax
When t = RC

## Slide 18
time
Battery voltage
voltage
0.63 Vmax
1 time constant
0.37 Vmax
2 time constants
0.37 x 0.37 Vmax
2 time constants
3 time constants
0.37 x 0.37 x 0.37 Vmax

## Slide 19: Time Constant
A measure of the time to charge a capacitor is called the time constant.
It is the time taken to rise to 63% of the maximum voltage…
…… ordrop to 37% of the maximum voltage or
drop 63% of the maximum voltage.

## Slide 20
time
Vmax
voltage
0.63 Vmax
1 τ
2τ
3 τ
0.372 Vmax
0.37 Vmax
{
{
0.373 Vmax
{

## Slide 21
Which capacitor charges faster?
Which circuit has the bigger time constant?
Which capacitor has the bigger capacitance?

## Slide 22: Do Now
The time constant for a capacitor charging circuit is 2.0 s. Find out:
The time taken for the voltage of the capacitor to reach 50% and 99% of its maximum respectively.

## Slide 23: Ans.

## Slide 24: How and why do R and C affect the time constant
τ is directly proportional to R and C.
If R increases, the current to charge/discharge the capacitor decreases. It will take longer time to charge/discharge a capacitor to/from the maximum voltage.
If C increases, it needs more charge to charge/discharge the capacitor, as Q =CV. It will take longer time to charge/discharge a capacitor to/from the same voltage.

## Slide 25: Do Now: Calculate time constant:
(1) R=2.26MΩ, C=100μF
(2) R=3.2kΩ, C=10000μF
(3) R=1.1MΩ, C=100μF
(4) R=1.02MΩ, C=100μF
(5) R=132kΩ, C=1000μF
(6) R=65kΩ, C=1000μF

## Slide 26
Battery voltage
Capacitor voltage
Electron flow continues until the capacitor voltage is equal (and opposite) to battery voltage

## Slide 27
VB
What is the relationship between VB VC and VR
VC
VR

## Slide 28
VB
VB = VC + VR
VC
VR

## Slide 29
As the capacitor charges, what happens to VB ?
VB
VC
VR
As the capacitor charges, what happens to VC ?
As the capacitor charges, what happens to VR ?
VB
VC
VR

## Slide 30: Charging Curves
Which curve represents charging voltage of the capacitor and which the resistor?
voltage
time
Vmax
VB
VC
VR
VC
VR

## Slide 31: Discharging a Capacitor
What happens when the switch is closed?

## Slide 32
VC
VR
As the capacitor discharges, what happens to VC ?
As the capacitor discharges, what happens to VR ?
Vmax
VC
VR

## Slide 33: Discharging Curves
Which curve represents discharging voltage of the capacitor and which the resistor?
voltage
time
Vmax
VC
VR
VC
VR

## Slide 34
VB
QTOT = C x V

## Slide 35
V
Capacitors in parallel
C2
C1
Q1
Q2

## Slide 36
V
Capacitors in parallel have the same voltage
QTOT = Q1 + Q2
CTOT V= C1V + C2V
CTOT = C1 + C2
Q1
Q2
VB = VC1 = VC2
Capacitors in parallel store more charge

## Slide 37
V
Capacitors in Series
V1
V2
C1
C2

## Slide 38
V
V = V1 + V2
Total capacitance is less than any of individual’s
Capacitors in series have the same charge, total voltage is the sum of individuals’.
V1
V2
C1
C2
Q = Q1 = Q2

## Slide 39: Connecting capacitors:
A capacitor is connected to a battery.
VB
QTOT = C x V

## Slide 40
The battery is disconnected.
What happens to the charge on the capacitor?
QTOT = C x V

## Slide 41
The capacitor is connected to an uncharged capacitor. What happens?
QTOT = C x V
elecrons
elecrons

## Slide 42
Closed loop so charge redistributes until the capacitors have the same voltage
QTOT = C x V
V1=V2

## Slide 43
capacitor discharge MIT

## Slide 44: Capacitor Construction

## Slide 45: The Capacitance depends on:
The Area of the plates
The separation of the plates.
εo is absolute permittivity of free space (vacuum or air)
εo =8.84x10-12 F m-1

## Slide 46
eg. Find the area needed to construct a 1 F capacitor using two parallel plates of 1 mm apart in air.
It is an area of 10000m x 10000m

## Slide 47: Dielectric
Putting an insulator between the plates increases the capacitance
εr is called dielectric constant, dimensionless.

## Slide 48: What does a dielectric do??
-
-
-
-
-
-
-
+
+
+
+
+
+
+

## Slide 49: Dielectric becomes polarised
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
The charges of the polarised dielectric attract more charges to the plates. Since the voltage does not change, the capacitance increases.

## Slide 50: More charge can be stored. Capacitance increases
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
More elecrons
More elecrons
-
-
-
-
-
+
+
+
+
+
+
+

## Slide 51
Capacitors

## Slide 52
Ceramic capacitor
Electrolytic capacitor

## Slide 53
When the capacitor is fully charged:
The flow of electrons stops;
Both plates have equal and opposite amount of charge;
The potential difference across the plates equals the supply voltage;
An electric field exists between the plates;
The strength of the electric field between the plates:
eg. A two parallel plate capacitor of 1mm apart is connected to a 12V battery. The electric field strength between the plates is:
E=12/0.001 =12000Vm-1

## Slide 54: Energy stored in a capacitor
When a capacitor is charged, it gains energy from the power source. The energy is stored as electric potential energy. When the capacitor is discharged, the potential energy is dissipated in the resistance of the circuit as heat and light.

## Slide 55
When a capacitor is charged to voltage V, with charge Q, the energy provided by the power =QV.
Voltage of Capacitor
V
Q Charge
The electric potential energy
stored by the capacitor

## Slide 56
A capacitor is labelled:
100 V 200 μF
    What does this mean?
    How much charge can it store?
    How much energy can it store?