## Slide 1: Electricity

## Slide 2: The charge of an electron e=1.6×10-19 Coulomb
How many electrons are needed to make 1 Coulomb?
6 x 1018
CAUTION
6,000,000,000,000,000,000 electrons

## Slide 3: Revision
Voltage is the energy gained or lost by one Coulomb of charge.
Current is the number of Coulombs flowing per sec.
Resistance is the number of volts needed to push one Amp of current

## Slide 5: Series Circuit
Adding resistors in series increases the resistance and decreases the current
2 A
6 V
1 A
6 V

## Slide 6: Parallel Circuit
Adding resistors in parallel decreases the resistance and increases the current
2 A
6 V
2 A
6 V
2 A
4 A

## Slide 7: Internal Resistance
If the wire’s resistance is 0.001 Ω, how much current flows?

## Slide 8
The battery has got some resistance inside itself.
We think of a battery like this:

## Slide 9
The chemical reaction causes the charge to gain energy (or voltage increase).
But it loses some energy (or voltage decrease) as it flows through because of the resistance.

## Slide 10
The gain in voltage is called the EMF
or electro motive force

## Slide 11
The voltage loss in the internal resistance is:
The output voltage of the cell is:

## Slide 12: Do Now: Ideal cell and real cell
Ideal cell: constant voltage output V without internal resistance (V=ε)
Real cell: output voltage drops when the current increases due to internal resistance r.

## Slide 13
When the current is zero, the output voltage is the EMF.
So the EMF can be thought of as the output voltage when the current is zero
i.e. if an AA cell is 1.5V, this is the EMF
0

## Slide 14
V
As the switches are closed, the current………
increases:
The voltage loss in the internal resistance ………..
increases
The output voltage goes ………
down

## Slide 15
Output Voltage
Current
EMF
Gradient =
r

## Slide 16
Explain what happens to the lamp’s brightness if the rheostat slider moves to the right.
R
I
Vo
Voltage across lamp
Power
Brightness
Ir
When the resistance of the rheostat increases, the total external resistance increases, and the current through the cell decreases. This leads to a smaller drop of voltage in the cell due to internal resistance. The voltage output of the cell increases, and there is more current going through the lamp. So the brightness of the lamp increases.

## Slide 17
Why do car headlights go dim when you start the engine?

## Slide 18
Why do car headlights go dim when you start the engine?
M
12 V
0.1 Ω

## Slide 19
Why do car headlights go dim when you start the engine?
Turn on the light
M
12 V
0.1 Ω
12 A
0.9 Ω
1.2 V
10.8 V

## Slide 20
Why do car headlights go dim when you start the engine?
Turn on the starter motor
M
12 V
0.1 Ω
60 A
0.9 Ω
6 V
6 V
0.1 Ω

## Slide 21
DC Circuits
Circuits can be very simple……

## Slide 22
Or complex …………

## Slide 23
But we can simplify them with ………
Kirchhoff’s Rules

## Slide 24
Point Rule
Current into a point equals current out as the number of charges are conserved
I1
I2
I1 + I2 =
I3
I3

## Slide 25
Loop Rule
Total voltage around a loop is zero as the energy gained equals the energy lost.
Voltage gained
Voltage lost
L
H
H
L

## Slide 26
Example
Voltage gained
Voltage lost
L
H
H
H
L
L
current

## Slide 27
We could go the other way around
Voltage gained
Voltage lost
L
H
L
L
H
H

## Slide 28
Cells are all 2.0 V, R1 = 3Ω, R2 = 1Ω
Find the current
First write a loop equation.
Solve: I = 0.5A
I

## Slide 29: Do Now: find the current
2A
I
5A
(a)
(b)
(c)

## Slide 30
I
I
Voltage decrease
Voltage gain
Voltage gain
Voltage decrease
L
H
L
H
L
H
L
H

## Slide 31: Multi Loop Circuits
Loop equation for top loop:
L
H
H
H
H
L
L
L

## Slide 32: Bottom Loop
L
H
L
L
H
H

## Slide 33: Outer Loop

## Slide 34: Point Equation

## Slide 35
The circuit diagram shows a battery operated cappucino frother.
Determine the battery voltage when the switch is open.
Explain what happens to the the battery voltage when the switch is closed.

## Slide 36
Battery voltage = 6.40 V
When the switch is closed, current flows in the circuit.
This current flows through the internal resistance.
This causes a voltage drop across the internal resistance
The output voltage is less than the EMF
  V0 = ε - Ir

## Slide 37
When the switch is closed, the battery voltage is 6.25 V, and the current flowing is 0.450 A.
Calculate the internal resistance.
Calculate the motor’s resistance.
V = ε – Ir
6.25 =6.4 – 0.45r

## Slide 38: This shows two frother batteries being charged

## Slide 39: Calculate the current in the charger.
Calculate the value of R.

## Slide 40: Write a loop equation for the top loop.

## Slide 41: Ans.
Use point rule: I = 0.250 + 0.208 =0.458A
Use outer loop to find R:
-6.4-0.25×1.5 -0.458R + 6.9 = 0
0.458R =6.9 - 6.4 -0.5×1.5
0.458R = 0.125
R =0.273Ω
For top loop
-6.4-0.25×1.5 +0.208×1.8 +6.4 = 0

## Slide 44
I1
I3
I2
Ans.
Point rule: I1= I2 + I3 (1)
Outer loop:
12 - 3I1- 5I3 = 0 (2)
Bottom loop
2 I2 + 4I2 - 5I3 = 0
or 6I2 - 5I3 = 0 (3)
(3) => I2 =5I3/6 (4)
(4) to (1)
I1= 5I3/6 + I3 or
6I1 = 11I3 or I1= 11I3/6 (5)
(5) to (2)
12 - 3× 11I3/6 – 5I3=0
12 - 11I3/2 – 5I3=0
I3=24/21=8/7A (6)
(6) to (5):
I1=11I3/6 =11×8/7/6 =88/42 =2.1A
Effective resistance
R = 12/2.1=5.7Ω
Standard equations:
I1- I2 - I3=0
3I1+0I2 + 5I3 = 12
0I1+ 6I2 - 5I3 = 0