## Slide 1: Electromagnetic Induction

## Slide 2: Electric Fields
Electric fields are created by charges
A charge in an electric field always has a force on it
+
force
force
-

## Slide 3: Magnetic Field
Magnetic fields are
created by magnets or
moving charges/current carrying wires.
Right-hand grip rule

## Slide 4
Magnetic Fields only affect moving charges
+
+
velocity
FORCE is…
ZERO
FORCE is…
towards you

## Slide 5
What is the direction of the current?

## Slide 6
strong field
weak field

## Slide 7
strong field
weak field

## Slide 8
N
S
electron beam
electron gun
x
y
z
Right-hand slap rule:
I’m number 1 (thumb in direction of current) (-y)
Fingers to field (direction) (x)
Palm to force (z)

## Slide 9
N
S
wire
Wire's velocity
x
y
z
I
I: z
Field: x
Force/velocity: y

## Slide 10
Mark the directions of the following magnetic fields
(a)
(f)
(e)
(d)
(c)
(b)
I
F
F
NB: (e) and (f) are in uniform magnetic fields

## Slide 11: Lenz’s Law
The induced current causes a force to oppose the change which produced it.
Conservation of energy: work has to be done to produce electricity.
G
S
N
G
S
N

## Slide 12
Current/EMF
time
Induced EMF in a moving loop
V=BvL

## Slide 13: Magnetic Flux
Magnetic flux is the amount of magnetic field.
It depends on the field strength and the area

## Slide 14
N
S
There is a large flux through this loop…
…and a smaller flux through this loop
…and an even smaller flux through this loop

## Slide 15
Which ring has the biggest magnetic flux in it?
Which ring has the strongest magnetic field strength in it?
Magnetic field lines

## Slide 16
Which ring has the largest magnetic flux in it?

## Slide 17
Magnetic Flux
= Magnetic Field Strength X Area
Webers (Wb) = Tesla x m2
Magnetic field strength is also called flux density.

## Slide 18
Which ring has the biggest magnetic flux ?

## Slide 19
Area is same
Field strength is same
Which ring has the biggest magnetic flux ?

## Slide 20
Year 12:
A wire cutting across a magnetic field has an induced EMF (or voltage)
Faraday’s Law
When the magnetic flux through a loop changes, there is an induced EMF (voltage)
The faster the change, the bigger the EMF

## Slide 22
A circular wire of area 0.10 m2, placed in a magnetic field of strength 0.80 T.
a. During 0.40 s the magnetic field is reduced to zero.
B= 0.80 T
i. How much flux initially passes through the coil?
ii. What is the size of the induced EMF in the coil as the magnetism field strength is reduced?
iii. What is the direction of the induced current?
b. With the magnetic field strength back to 0.80 T, the loop is rotated ¼ turn about its vertical axis. The average induced voltage is 0.4 V.
i. What is the change in flux through the loop during ¼ turn?
ii. How long does it take the loop to do the ¼ turn?

## Slide 23
Ans.

## Slide 24: Changing the Flux
You can change the flux by changing the field strength or the area perpendicular

## Slide 25
N
S
Changing the field strength

## Slide 26
N
S
Changing the area

## Slide 27
N
S
Changing the area perpendicular

## Slide 28
Flux Change in a Generator

## Slide 29
For many loops
becomes

## Slide 30
Changing the actual area Changing the angle
Changing the Area

## Slide 31
Flux vs time for a moving loop
flux
time
When did the Flux change?

## Slide 32
voltage
time
Induced EMF for a moving loop

## Slide 33
voltage
time
time
flux

## Slide 34
Close switch… current increases …field increases
Flux change through 2nd coil
Induced EMF in 2nd coil
Creates current in 2nd coil
Creates magnetic field that opposes the cause.
N
N

## Slide 35
Faraday: A flux change causes an induced EMF (voltage)
Lenz’s Law states that the induced voltage opposes the flux change that caused it.

## Slide 36: Lenz’s Law
Electron flow
Force on roller
1: electrons in roller are moving
2: causing them to be pushed
3: electrons in roller are now flowing
4: causing them (and roller) to be pushed

## Slide 37
N
S
The induced magnetic field always opposes the magnetic field that causes it
N
electrons

## Slide 38
N
S
Pulling a North pole away induces a South pole on the left side.
N
electrons

## Slide 39
N
Falling magnet creates a flux change in the pipe.
This creates induced EMF
This creates induced current
This creates induced magnetic field
Induced magnetic field opposes flux change

## Slide 40: So how does your electric toothbrush charge up?

## Slide 41
Increasing current in Primary
Causes flux change in core
Causes flux change in Sec
Causes induced EMF in Sec
Causes induced current in Sec
This is called Mutual Induction
P
S

## Slide 42: AC Generator
http://www.walter-fendt.de/ph11e/generator_e.htm

## Slide 43
B
A
C
D
Voltage
Angle
Flux
Angle
Coil position (End on)

## Slide 44
Voltage
Angle
S
N
S
Flux
Angle

## Slide 45
Voltage
Angle
S
N
Flux
Angle
S

## Slide 46
Voltage
Angle
S
N
S
Flux
Angle

## Slide 47
Voltage
Angle
S
N
S
Flux
Angle

## Slide 48
Voltage
Angle
S
N
S
Flux
Angle

## Slide 49: Self Inductance Physical Laboratory\Electromagnetism:\
C:\Program Files\PhET-1.0\simulations\faraday
C:\Program Files\PhET-1.0\C:\Program Files\PhET-1.0\simulations\faraday\faraday.jarsimulations\faraday